## Slide 1
Lab Book 0.1. ModeSolver
Student:

## Slide 2: Instructions General
SOFTWARE
Python notebook supplied by instructors
SCRIPTS
From poliformat  download the 010_MODESOLVER_v2025_Student.ipynb
Either run locally or at Google Collaboratory
We are going to work with different Cross-Sections. In general, we will need: Materials definitions and the Geometrical parameters of each Cross-section.
XY Cross-section
h
(height)
W (width)
Core
Cladding
W (width)
Core
Cladding
Slab
h_slab
h_core
shallow waveguide
deep waveguide

## Slide 3: Learning outcome #1 – Effective index of a waveguide
INSTRUCTOR:
Present Python and GDSFactory: materials, output, results.
Explain how to run a simulation for a particular cross-section.
Showcase how to change between shallow and deep waveguide.
Describe how to change the wavelength and width for the waveguide analysis.
Describe the outputs.
ALL EXAMPLE #1: waveguide width 1.2 µm, deep wvg, wavelength start and end same 1.55 µm  all ”Run”
ALL: Follow instructor, that will show how to 1) plot mode, 2) explore the results (neff …)
Document all your results (neff, plot fields of different modes, comparison between different polarizations…)

## Slide 4: Learning outcome #2 – Wavelength behavior Wavelength 1.5-1.6 µm (step 0.02 µm) – width 1.2 µm
Comment results (neff changes this way with wavelength, comparison between different waveguide cross-sections …)
shallow waveguide
Paste plot here
deep waveguide
Paste plot here
slab = 150nm

## Slide 5: Learning outcome #3 – Width dependence Width 0.6 - 1.6 µm (step 0.1 µm) – Wavelength 1.55 µm
Comment results (neff changes this way with wavelength, comparison between different waveguide cross-sections …)
deep waveguide
Paste plot here

## Slide 6: Thank you