## Slide 1
Lab Book 1.0. Waveguides
Student:

## Slide 2: Instructions General
SOFTWARE
Python notebook supplied by instructors
SCRIPTS
From Poliformat  download the 10_WAVEGUIDES_v2025_Student.ipynb
Either run locally or at Google Collaboratory
h
(height)
W (width)
Core
Cladding
W (width)
Core
Cladding
Slab
h_slab
h_core
shallow waveguide
deep waveguide

## Slide 3: Learning outcome #1 – Convergence tests SH & DE waveguide, w = 1.2 µm, neff_TE0, wvl 1.55 µm. Change grid_resolution from 6 to 150 (Set your own spacing between points).
deep waveguide
Paste neff_TE0 vs grid_resolution plot here
shallow waveguide
Paste neff_TE0 vs grid_resolution plot here
Comment results, determine above which grid value the effective index calculation does not change significantly
slab = 150nm

## Slide 4: Learning outcome #2 – Mode confinement with wavelength deep waveguide (w=0.8 µm) - wavelengths from 1.5 µm to 1.8 µm. Use the .mode_area() parameter of the gt.modes.Waveguide() function for this analysis.
Comment results, not only graphic ones, but also the associated effective index with respect to the core and cladding material indices
deep waveguide
Paste modal plots at 1.5 µm and 1.8 µm
deep waveguide
Paste Mode area vs wavelength plot here

## Slide 5: Learning outcome #3 – Group index calculation LO#2 Lab 0.1. Wavelength 1.5-1.6 µm (step 0.02 µm), width 0.8-1.2 µm (0.1 µm step). Calculate ng
Comment results, group index variation over wvl (if any) then comparison of values between shallow and deep waveguide
deep waveguide
Paste ng vs wavelength plot here
shallow waveguide
Paste ng vs wavelength plot here
slab = 150nm

## Slide 6: Learning outcome #4 – Waveguide compact model Let’s model the waveguide using a second order polynomial:
Find the second-degree polynomial coefficients and relate them with the group index and the dispersion parameter.
Comment on the results found for the TE0 and TM0 for both deep and shallow waveguides.
deep waveguide
neff_TE0 vs with the second-degree polynomial fit
& neff_TM0 vs with the second-degree polynomial fit
shallow waveguide
neff_TE0 vs with the second-degree polynomial fit
& neff_TM0 vs with the second-degree polynomial fit
slab: 150nm

## Slide 7: Learning outcome #5 – Bend waveguide radius vs. loss – deep Find neff_TE0 & neff_TM0 for wvl 1.55 µm, width 1.0 µm for R=25,50,75,100, 125,150 µm
Comment results, which is the safe radius, consider safe means less than 0.1 dB/90º.
deep waveguide
Paste dB/90º neff_TE0 & neff_TM0 vs R

## Slide 8: Thank you